## Slide 1: Smart Automated STEM
Gerd Duscher
For MLSTEM 2024 workshop
Main developer of technique:
Austin Houston, Utkarsh Pratiush

## Slide 2: Maximal Possible Information in STEM
sample
diffraction pattern
(different convergence angles or only parts),
low-loss EELS,
core-loss EELS
(several energy-windows),
EDS,
Others
(like Cathodoluminescence or secondary electrons)
For
Different volume sizes
Different angles
Ideally with knowledge of number
of incoming electrons

## Slide 3: Current State of the Art
sample
For
one volume size
one tilt angle
small area
diffraction pattern
(only part of pattern
- HAADF:large angles),
one STEM condition
- EDS spectrum
- EELS (high- and low-loss)
- diffraction pattern

## Slide 4: Current Data Collection Strategies
Spectrum Imaging, 4D-STEM:
  Grid Scan:
  Fully filled matrix
  Usually: 90% of data points are unimportant
Compressed sensing (also known as compressive sensing, compressive sampling, or sparse sampling)
  (more or less) random selection of points used to interpolate whole dataset.
  Sparse matrix
  Important parts may be missed

## Slide 5: Alternative Data Collection Strategies
Select data points smartly
  Use all possibilities of machine learning discussed in this workshop
  And select the points of interest.
Collect data remotely
Select various of all available signals of a STEM
Avoid investment in infrastructure and instrument time to collect a lot of data that are never used.

## Slide 6: Minimum Requirement for Smart Acquisition
Overview image
Drift Correction
Algorithm to select points
  Complexity depends only on computing power
Ability to collect data at selected points

## Slide 7: Minimum Requirement for Smart Acquisition for EELS
Get image
Shift beam
Get spectrum
Nice to have but not immediately necessary:
Drift
Set dispersion and energy offset
Get dispersion and energy offset once

## Slide 8: Implementation in Digital Micrograph
Make a server software in python
  Acquire digiscan image
  Set beam position
  Get (part) of ccd camera
  This functionality is readily available in DM
  Several server software packages available in python

## Slide 9: Implementation of Smart Collection

## Slide 10: The client
Can be any remote computer
Can be a supercomputer to provide enough computing power for on-the-fly machine learning algorithms.
Jupyter notebook: so data are directly accessible to all python packages

## Slide 11: Example
Acquisition of single spectrum is 2 times slower for low loss than in spectrum image.
Acquisition of 1/10000 data points in grid scan.

## Slide 12: Advantages
Truly large areas can be investigated
Mostly relevant data points chosen for acquisition
Variation of method to determine data points
  Active Learning
  Clustering
  Edge detection
  DCNN
  …
Learning algorithms can be applied to increasing data volume

## Slide 13: Further Development
Keep STEM at optimum condition
Change STEM optics and detectors
  Get diffraction and EELS spectra from same sub pixel areas
Smart drift correction
Get metadata
Develop methods for correlated data

## Slide 14: Human in the Loop Workflow

## Slide 15: Human in the Loop Workflow